## Slide 1: Scale formation

## Slide 2: Problem definition

## Slide 3: Problem definition
Scale formation in pipelines (CaCO₃, BaSO₄, SrSO₄)
Operational Impact
Reduces flow efficiency.
Increases pressure drop.
Accelerates corrosion.
Raises maintenance and operational costs.
Requirements:
Predicts scale formation and its location
Identify Type of scale and its severity
Optimization of scale inhibitor dosing.

## Slide 4: Kinetic Models

## Slide 5
# | Focus | System / Domain | Scale Type | Methodology | Inhibitor, Dosage
1 | scale deposition kinetics | Reservoir + pipeline | CaCO₃, BaSO₄, FeCO₃ | Coupled thermodynamic–kinetic + transport equations | -
2 | CaCO3 precipitation kinetics on steel pipe and inhibition kinetics | Carbon steel pipe / tubing; flowing pipe reactor | CaCO3 | Plug-flow reactor + mass transfer modeling | MIC + inhibitor retention (“memory effect”)
3 | Effect of Ca²⁺ / HCO₃⁻ on kinetics + inhibitor performance | Pipeline (dynamic loop) | CaCO₃ | Dynamic tube blocking tests | MIC, inhibitor ranking depends on water chemistry
4 | Surface scaling kinetics + real-time visualization | Pipe surface (flow cell) | CaCO₃, BaSO₄ | In-situ imaging + flow rig | bulk MIC can aggravate surface scaling
5 | Effect of turbulence on barite precipitation and inhibition. | Pipeline (tubing + valves) | BaSO₄ | Experimental tubing system | turbulence can increase precipitation kinetics in the presence of inhibitor and affect optimal dose development

## Slide 6
# | Focus | System / Domain | Scale Type | Methodology | Inhibitor, Dosage
6 | Theoretical model for induction time & inhibitor dosage | General (lab + model) | CaCO₃, BaSO₄ | CNT-based kinetic model | Predict minimum effective dosage
7 | Kinetic scale prediction with flow dynamics (FFD + CFD) | Full production system (pipelines, tubing, valves) | CaCO₃, BaSO₄, SrSO₄ | CFD + kinetic model + lab + field validation | Links kinetics to inhibitor demand
Main Conclusions
Thermodynamic prediction (SI) alone is fundamentally insufficient
Flow regime (shear, turbulence, velocity) is a primary driver of scaling
Inhibitor dosage depends on water chemistry, flow regime, temperature and pressure
Inhibitor delay before becomes effective
Induction time is a key operational variable for predicting onset and scheduling inhibitor dosing
Existing models are static, lab-based, and not integrated with real-time field data

## Slide 7
How they determine MIC
Observer whether precipitation resumes after inhibitor pretreatment, and measure protection times after known inhibitor exposures
Blank (no inhibitor) to determine the baseline time to blockage, test inhibitor concentrations and define MIC from the lowest dose that passes the tube-blocking criterion.
Add inhibitor and determine the critical saturation index needed to induce precipitation under each flow regime.
Predicted mechanistically from induction-time modeling or kinetic/critical-SR

## Slide 8
Ref
Zhang, P., Liu, Y., Kuok, S. C., Kan, A. T., & Tomson, M. B. (2019). Development of modeling approaches to describe mineral scale deposition kinetics in porous medium and pipe flow system. Journal of Petroleum Science and Engineering, 178, 594-601.
Zhang, N., Kan, A., Shi, W., Alsaiari, H., & Tomson, M. B. (2012, May). A novel approach to the study of CaCO3 precipitation kinetics on carbon steel pipe. In SPE International Oilfield Scale Conference and Exhibition (pp. SPE-155263). SPE.
Xu, B., Chen, T., Chen, P., Montgomerie, H., Hagen, T., Guo, Q., & Yang, X. (2014, May). Influence of Calcium and Bicarbonate Ions on the Kinetics of CaCO3 Formation at High Temperature in the Absence and Presence of Scale Inhibitors. In SPE International Oilfield Scale Conference and Exhibition (p. D021S007R002). SPE.
Sanni, O., Bukuaghangin, O., Charpentier, T., Kapur, N., & Neville, A. (2016, May). Using a real-time visualisation technique for the assessment of surface scale kinetics and mechanisms of inhibition. In SPE International Oilfield Scale Conference and Exhibition (pp. SPE-179896). SPE.
Yan, F., Zhang, F., Bhandari, N., Ruan, G., Alsaiari, H., Dai, Z., ... & Tomson, M. (2017, April). The effect of turbulence on mineral scale control in oilfield. In SPE International Conference on Oilfield Chemistry? (p. D021S006R002). SPE.
Dai, Z., Zhang, F., Yan, F., Bhandari, N., Ruan, G., Zhang, Z., ... & Tomson, M. (2017, April). A new theoretical model for the induction time and scale inhibitor dosage predictions for calcite and barite over wide ranges of temperature, inhibition concentration and saturation index. In SPE International Conference on Oilfield Chemistry? (p. D031S009R004). SPE.
Stalker, R., Nichols, D., Fyfe, A., Zarareh, A., Boyde, D., & Graham, G. (2024, November). Advances in inorganic scale prediction–development and validation of a kinetic model. In Abu Dhabi International Petroleum Exhibition and Conference (p. D021S045R001). SPE.

## Slide 9: Transport - Deposition Approaches

## Slide 10
# | Focus | System / Domain | Scale Type | Methodology | Inhibitor, Dosage
1 | Scaling tendency prediction | Gas production tubing + flowline | FeS, FeCO₃ | Semi-empirical + mechanistic (corrosion + precipitation + erosion, ST ratio) | -
2 | Effect of turbulence on deposition & inhibition | Turbulent regions (valves, chokes, near-well) | BaSO₄ | Experimental (rotating cylinder, high Reynolds number) | Mechanism-dependent performance; dosage not simply ↑ with turbulence
3 | Integrated deposition + inhibitor prediction | Tubing / flow systems | BaSO₄, CaCO₃ | Hybrid model (thermodynamics + kinetics + transport + adsorption) | Predicts minimum inhibitor dosage (Langmuir adsorption model)
4 | Inhibitor evaluation under turbulent flow | Subsea pipelines | CaCO₃ | Experimental | Direct MIC determination
5 | Inhibitor transport in pipelines | Oil-water trunkline + multiple flowlines | General inorganic scales | CFD | Predicts inhibitor distribution
6 | Surface vs bulk scaling mechanisms | General pipelines / equipment surfaces | CaCO₃, BaSO₄ | Mechanistic + experimental review (nucleation, growth, MIC concepts) | Conceptual (MIC_bulk vs MIC_surface)

## Slide 11
# | Focus | System / Domain | Scale Type | Methodology | Inhibitor, Dosage
7 | Coupled transport of inhibitor + scaling ions | Trunkline with multiple flowlines | General | CFD | Enables optimization of injection rate & location
8 | Scaling rate prediction in pipelines | Wet-gas pipelines | CaCO₃ BaSO₄, SrSO₄ | CFD + reaction kinetics + particle transport | -
Main Conclusions
Bulk scaling predictions significantly underestimate real pipeline scaling risk
  Bulk precipitation ≠ surface deposition
Deposition is controlled by mass transfer, not just reaction kinetics
Inhibitor performance depends on adsorption, not just concentration
Current models require high-quality input data (practical limitation)

## Slide 12
How they determine MIC
Evaluates inhibitor performance by how much deposition remains under different turbulent conditions
fit the inhibitor effect using mathematical model, predict MIC by solving for required protection time, or maximum allowable deposition thickness rate.
Incrementally increasing inhibitor concentration, pressure drop no longer increases significantly.
trial-and-error / scenario-based optimization
parametric sweep / threshold search

## Slide 13
Ref
Santoso, R. K., Rahmawati, S. D., Gadesa, A., & Wahyuningrum, D. (2017, July). Scale build-up prediction of FeS and FeCO3 in gas production pipes. In Journal of Physics: Conference Series (Vol. 877, No. 1, p. 012029). IOP Publishing.
Chen, T., Chen, P., Montgomerie, H., Hagen, T., Benvie, R., Guo, Q., ... & Yang, X. (2014, May). Do we need higher dose scale inhibitors to inhibit scale under turbulent conditions? Insight into mechanisms and new test methodology. In SPE International Oilfield Scale Conference and Exhibition (p. D011S004R003). SPE.
Dai, Z. J., Kan, A., Lu, Y. T. A., Leschied, C., Zhao, Y., Dai, C., ... & Tomson, M. (2021, November). Novel Mineral Scale Deposition Model Under Different Flow Conditions with or Without Scale Inhibitors. In SPE International Conference on Oilfield Chemistry? (p. D021S009R002). SPE.
Pimentel, D., Kan, A., Ye, Y., Wang, X., Reiss, A., Deng, G., ... & Tomson, M. (2024, June). Methodology to Evaluate Calcite Scale Inhibitors Under Turbulent Flow for Subsea Oilfield Production Applications. In SPE International Oilfield Scale Conference and Exhibition (p. D023S009R004). SPE.
Liu, M., Chen, T., Rached, R., & Zhao, W. (2025, April). Numerical Simulation of Transient Transport of Scale Inhibitor in an Oil-Water Trunkline with Multiple Flowlines. In SPE Gas & Oil Technology Showcase and Conference (p. D012S006R002). SPE.
Rodriguez-Hernandez, C. D., Chen, T., Liu, M., Shafi, M., Rached, R., Alfaleh, K., & Zhao, W. (2025, November). Transport Modeling of Scale Inhibitor and Scaling Ions in an Oil-Water Trunkline with Multiple Flowlines. In Abu Dhabi International Petroleum Exhibition and Conference (p. D021S067R005). SPE.
Neville, A. (2012). Surface scaling in the oil and gas sector: Understanding the process and means of management. Energy & fuels, 26(7), 4158-4166.
Li, C., Wang, B., Jia, W., & Li, G. (2020). Predicting the scaling rate of calcium carbonate in wet-gas pipes via a CFD method. Desalination and Water Treatment, 197, 14-29.

## Slide 14: Inhibitor modeling

## Slide 15
# | Focus | System / Domain | Scale Type | Methodology | Inhibitor, Dosage
1 | Kinetics + inhibition mechanism | Pipe flow system (lab-scale, flow loop) | CaCO₃, CaSO₄ | Mechanistic kinetic model (nucleation + growth + adsorption) | Scale mass vs time, rate constants, activation energy
2 | Inhibitor dosage prediction (MIC) | Oilfield (lab + field validation) | BaSO₄, CaCO₃ | Hybrid (experimental + semi-empirical + CNT-based models) | Minimum Inhibitor Concentration (MIC), induction time
3 | Inhibitor screening + dosage methodology | Oilfield (EOR + lab dynamic systems) | CaSO₄ | Experimental + semi-empirical modeling (mCSTR, mKTT) | Induction time vs concentration, dosage estimation
4 | Deposition kinetics + inhibition mechanism | Flow loop (pipeline-like tubing) | BaSO₄ | Mechanistic + Langmuir adsorption model | Deposition rate constants, inhibition efficiency vs concentration
Field vs lab gap

## Slide 16
How they determine MIC
induction time models
It is the time between when a solution becomes supersaturated and when detectable crystals (scale) appear.

## Slide 17
Ref
Al-Roomi, Y. M., & Hussain, K. F. (2016). Potential kinetic model for scaling and scale inhibition mechanism. Desalination, 393, 186-195.
Dai, C., Dai, Z., Zhang, F., Zhao, Y., Deng, G., Harouaka, K., ... & Tomson, M. (2019, March). A unified experimental method and model for predicting scale inhibition. In SPE International Conference on Oilfield Chemistry? (p. D011S006R004). SPE.
Paudyal, S., Mateen, S., Dai, C., Ko, S., Wang, X., Deng, G., ... & Tomson, M. B. (2020, June). Developments on calcium sulfate scaling prediction and control in oil and gas production. In SPE International Oilfield Scale Conference and Exhibition (p. D031S005R001). SPE.
Lu, A. Y. T., Shi, W., Wang, J., Venkatesan, R., Harouaka, K., Paudyal, S., ... & Tomson, M. (2019). The mechanism of barium sulfate deposition inhibition and the prediction of inhibitor dosage. Journal of Chemical & Engineering Data, 64(11), 4968-4976.

## Slide 18: ML / Scale Tendency

## Slide 19
# | Focus | System / Domain | Scale Type | Methodology | Outputs
1- 5 | Scale tendency | Reservoirs / Production well | CaCO₃, CaSO₄ BaSO₄ | Decision Tree Random Forest Multilayer Perceptron CNN K-Nearest Neighbors Support Vector Machine Logistic Regression Naïve Bayes Adaptive Boosting Ensemble Learning | Binary classification ‘Scale / No scale’

## Slide 20
Ref
Al-Hajri, N. M., Al-Ghamdi, A., Tariq, Z., & Mahmoud, M. (2020). Scale-prediction/inhibition design using machine-learning techniques and probabilistic approach. SPE Prod Oper 35: 0987–1009.
Ugoyah, J. C., Ajienka, J. A., Wachikwu-Elechi, V. U., & Ikiensikimama, S. S. (2022, August). Prediction of scale precipitation by modelling its thermodynamic properties using machine learning engineering. In SPE Nigeria Annual International Conference and Exhibition (p. D021S007R005). SPE.
Yousefzadeh, R., Bemani, A., Kazemi, A., & Ahmadi, M. (2023). An insight into the prediction of scale precipitation in harsh conditions using different machine learning algorithms. SPE Production & Operations, 38(02), 286-304.
Al-Hatmi, A. R. (2023). Application of Machine Learning Techniques For Inorganic Scale Precipitation Prediction in a Sandstone Reservoir. Sultan Qaboos University (Oman).
Ferreira, B. X., Barbosa, C. R. H., Cajaiba, J., Kartnaller, V., & Santos, B. F. (2022). Development of artificial neural network models for the simulation of a CaCO3 Scale formation process in the presence of monoethylene glycol (MEG) in dynamic tube blocking test equipment. Energy & Fuels, 36(4), 2288-2299.

## Slide 21: ML / Scale Thermodynamics

## Slide 22
# | Scale type | Algorithm | Input | Output | Application
1 | CaCO₃ | Least Squares SVC Radial Basis Function GA | Pressure, Temperature | Dissolved CaCO₃ | reservoirs
2 | SrSO₄ BaSO₄ | Generalized Additive Model Random Forest, Decision Tree MLP, LSTM, CNN–LSTM, SVM–RF, MLP–DT | Pressure, Temperature, NaCl, CaCl₂, MgCl₂, Ionic strength Electrolyte composition | Sulfate mineral solubility SrSO₄, BaSO₄ | Pipeline
3 | CaSO₄ CaCO₃ BaSO₄ CaCO₃ SrSO₄ NaCl SiO₂ FeCO₃ | Multiple Linear Regression Random Forest Extreme Gradient Boosting Decision Trees | Ba²⁺, Ca²⁺, Cl⁻, Cu²⁺, Fe²⁺ / Fe³⁺, K⁺, Mg²⁺, Na⁺ Pb²⁺, S, Si, Sr²⁺, Zn²⁺, HCO₃⁻, SO₄²⁻, | Saturation Index | Well
4 | BaSO₄, CaSO₄ | Statistical Neural Network Multilayer Perceptron (MLP) | Temperature, Pressure | BaSO₄, CaSO₄ | Well
5 | BaSO₄, SrSO₄ | DNN | Temperature, Pressure, Oil rate, Water Rate, Injection Gas, Gross Gas, Ca, Mg, Ba, St, Su, TDS | Weight percentage (%) of BaSO₄ or SrSO₄ in deposited scale sample Binary classificatuion | reservoirs

## Slide 23
Ref
Ahmadi, M. A., Bahadori, A., & Shadizadeh, S. R. (2015). A rigorous model to predict the amount of dissolved calcium carbonate concentration throughout oil field brines: side effect of pressure and temperature. Fuel, 139, 154-159.
Cao, Z., Hu, Y., & Zhang, P. (2024). Predicting sulfate mineral scale solubility with machine learning. Journal of Cleaner Production, 461, 142655.
Askar, M. M., Ela, M. A. E., El-Banbi, A. H., & Sayyouh, M. H. (2025). Development of machine learning models for predicting the deposition of sulfide scales in oil production wells. Journal of King Saud University–Engineering Sciences, 37(7), 1-34.
Askar, M. M., El Ela, M. A., El-Banbi, A. H., & Sayyouh, M. H. (2024, November). Predicting scale depositions of barium and strontium sulfates using novel artificial neural network algorithms. In Abu Dhabi International Petroleum Exhibition and Conference (p. D021S045R006). SPE.
Belkacem, O., Rezrazi, A., Aizi, K., Abdelouahed, L., Laidi, M., Touil, A., ... & Hanini, S. (2025). Prediction of barite scale formation and inhibition in hydrocarbon reservoirs using AI modeling: Focus on different optimization algorithms. Results in engineering, 26, 105222.

## Slide 24: ML / Scale thicknes

## Slide 25
# | Focus | System / Domain | Scale Type | Methodology | Outputs
1-9 | Scale thickness prediction and detection under varying flow conditions | pipelines / flowlines (multiphase flow systems) with some simplified regimes | CaCO₃, CaSO₄ | AI/ML (ANN, DNN, GMDH, MLP) combined with gamma/neutron radiation-based sensing and MCNP simulations | Scale thickness (concentric/eccentric), sometimes fluid volume fractions
Invers model from flow, temperature to scale thickness
No inhibitor modeling or dosage optimization

## Slide 26
Ref
Carvalho, A. C. L., Salgado, W. L., Dam, R. D. F., Conti, C. C., & Salgado, C. M. (2024). Calcium carbonate scale thickness prediction in annular three-phase flow using gamma-ray densitometry and artificial neural networks. Radiation Physics and Chemistry, 223, 112018.
Salgado, C. M., Salgado, W. L., de Freitas Dam, R. S., & Conti, C. C. (2021). Calculation of scales in oil pipeline using gamma-ray scattering and artificial intelligence. Measurement, 179, 109455.
Salgado, W. L., de Freitas Dam, R. S., Puertas, E. J. A., & Salgado, C. M. (2025). Predicting scale thickness in three-phase flow using neutron activation analysis and deep learning. Measurement, 242, 115880.
de Freitas Dam, R. S., Salgado, W. L., Schirru, R., & Salgado, C. M. (2022). Application of deep neural network and gamma-ray scattering in eccentric scale calculation regardless of the fluids volume fraction inside a pipeline. Applied Radiation and Isotopes, 188, 110353.
de Freitas Dam, R. S., Dos Santos, M. C., Salgado, W. L., da Cruz, B. L., Schirru, R., & Salgado, C. M. (2023). Prediction of fluids volume fraction and barium sulfate scale in a multiphase system using gamma radiation and deep neural network. Applied Radiation and Isotopes, 201, 111021.
Iliyasu, A. M., Mayet, A. M., Hanus, R., El-Latif, A. A. A., & Salama, A. S. (2022). Employing GMDH-type neural network and signal frequency feature extraction approaches for detection of scale thickness inside oil pipelines. Energies, 15(12), 4500.
Chen, T. C., Iliyasu, A. M., Hanus, R., Salama, A. S., & Hirota, K. (2022). Predicting scale thickness in oil pipelines using frequency characteristics and an artificial neural network in a stratified flow regime. Energies, 15(20), 7564.
Alamoudi, M., Sattari, M. A., Balubaid, M., Eftekhari-Zadeh, E., Nazemi, E., Taylan, O., & Kalmoun, E. M. (2021). Application of gamma attenuation technique and artificial intelligence to detect scale thickness in pipelines in which two-phase flows with different flow regimes and void fractions exist. Symmetry, 13(7), 1198.
Chen, T. C., Iliyasu, A. M., Alizadeh, S. M., Salama, A. S., Eftekhari-Zadeh, E., & Hirota, K. (2023). The use of artificial intelligence and time characteristics in the optimization of the structure of the volumetric percentage detection system independent of the scale value inside the pipe. Applied Artificial Intelligence, 37(1), 2166225.

## Slide 27: Similar applications

## Slide 28
# | Focus | System / Domain | Scale Type | Methodology | Notes
1 | ML framework for scale prediction and prevention | Offshore production / well operations | CaCO₃, MgSO₄ | GAN-based machine learning + SCADA + sensors | 
2 | Near real-time scale monitoring | Wells and production facilities | BaSO₄ | Thickness Shear Mode Resonator (TSMR) sensor | 
3 | Combined scale/corrosion inhibitor optimization | Subsea flowlines & topside facilities | BaSO₄, CaCO₃ | Field monitoring + laboratory testing + TSMR | 
4 | In-situ real-time scale detection | Flowlines & production systems | CaCO₃ | ATR spectroscopy sensor | 
5 | Smart flow assurance management system | Field-wide (700+ wells) | Multiple scales | Integrated software platform + dashboards | 
6 | ML thermodynamic water-property prediction | General oilfield applications | 11 scale minerals | CatBoost reduced-order ML models trained on thermodynamic simulations | 
7 | Comprehensive scale management strategy | Surface facilities & flowlines | BaSO₄ (primary), CaCO₃ | Scale prediction + Power BI + Scale Risk Factor (SRF) | 

## Slide 29
# | Focus | System / Domain | Scale Type | Methodology | Notes
8 | Field evaluation of antiscalants | Seawater RO plant | CaCO₃, CaSO₄, BaSO₄, SrSO₄ | Bench-scale testing + full-scale plant performance monitoring | 
9 | Real-time optimization | Brackish water RO | CaCO₃ | Dynamic control algorithm + pilot RO validation | 
10 | Physics-based prediction & dosage modeling | Membrane systems | CaCO₃, CaSO₄, BaSO₄, SrSO₄, silica, Ca phosphate | Ion-association thermodynamic model + induction-time model | 
11 | AI prediction of pipeline deposition | Oil pipeline | Wax | OLGA simulation + RRR wax model + Stacked Autoencoder (SAE) | Prediction Target : Wax location and thickness

## Slide 30
Ref
Arukhe, J. O., Ghamdi, K. A., & Anazi, A. F. (2025, April). Machine Learning Framework for Treating and Preventing Scale Formation. In Offshore Technology Conference (p. D041S056R002). OTC.
Emmons, D. H., Graham, G. C., Holt, S. P., Jordan, M. M., Locardel, L. P., & Locardel, B. (1999, October). On-site, near-real-time monitoring of scale deposition. In SPE Annual Technical Conference and Exhibition? (pp. SPE-56776). SPE.
Jordan, M. M., Archibald, I., Donaldson, L., Stevens, K., & Kemp, S. (2003, February). Deployment, Monitoring and Optimisation of a Combined Scale/Corrosion Inhibitor within a Subsea Facility in the North Sea Basin. In SPE International Conference on Oilfield Chemistry? (pp. SPE-80214). SPE.
Smith, J. K., Yuan, M., Lopez, T. H., Means, M., & Przybylinski, J. L. (2004). Real-time and in-situ detection of calcium carbonate scale in a west Texas oil field. SPE Production & Facilities, 19(02), 94-99.
Jain, A., Patel, N., Hammonds, P., & Pandey, S. (2018, October). A smart software system for flow assurance management. In SPE Asia Pacific Oil and Gas Conference and Exhibition (p. D022S006R007). SPE.
Farrell, J., & Makarychev-Mikhailov, S. (2023, June). Water digital avatar—where chemistry is mixed with machine learning. In SPE International Conference on Oilfield Chemistry? (p. D011S004R006). SPE.
Ness, G., Langvik, M., & Ree, L. S. (2024, June). How to Develop a Comprehensive Scale Management Strategy and Use the Scale Risk Factor (SRF) for Chemical Optimisation. In SPE International Oilfield Scale Conference and Exhibition (p. D013S004R001). SPE.

## Slide 31
Ref
Al-Shammiri, M., Safar, M., & Al-Dawas, M. (2000). Evaluation of two different antiscalants in real operation at the Doha research plant. Desalination, 128(1), 1-16.
Mangal, M. N., Yangali-Quintanilla, V. A., Salinas-Rodriguez, S. G., Dusseldorp, J., Blankert, B., Kemperman, A. J., ... & van der Meer, W. G. (2022). Application of a smart dosing pump algorithm in identifying real-time optimum dose of antiscalant in reverse osmosis systems. Journal of membrane science, 658, 120717.
Ferguson, R. J., Ferguson, B. R., & Stancavage, R. F. (2011). Modeling scale formation and optimizing scale inhibitor dosages in Membrane Systems. In RJ Ferguson, BR Ferguson, RF Stancavage/AWWA Membrane Technology Conference.—2011.
Kim, J., Han, S., Seo, Y., Moon, B., & Lee, Y. (2022). The development of an AI-based model to predict the location and amount of wax in oil pipelines. Journal of Petroleum Science and Engineering, 209, 109813.

## Slide 32: Pipe monitoring

## Slide 33
# | Focus | Approach | Main Application
1 | Review of guided-wave structural health monitoring (SHM) methods for reliable pipeline monitoring under varying environmental and operational conditions. | Ultrasonic guided waves (UGW), SHM, baseline compensation, machine learning (PCA, ICA, SVD, ANN, SVM), signal processing, and false-alarm mitigation. | Continuous pipeline integrity monitoring, defect detection, and robust SHM under real operating conditions.
2 | Comprehensive review of pipeline monitoring, inspection, and fitness-for-service (FFS) assessment technologies for oil and gas pipeline networks. | In-line inspection (MFL, UT, eddy current, IMU), optical fiber sensing (DAS, Φ-OTDR, OFDR), guided waves, SCADA, AI/machine learning, multi-sensor fusion, and FFS assessment. | Pipeline integrity management, leak detection, defect inspection, optical fiber monitoring, AI-assisted monitoring, and FFS assessment.
3 | Development of an ultrasonic nondestructive method to measure scale thickness on the inner surface of pipes. | Pulse-echo ultrasonic testing using time-of-flight (TOF) measurements between the pipe/scale and scale/fluid interfaces to calculate scale thickness. | Nondestructive in-situ measurement of internal pipe scale thickness (laboratory validation on PP, PVC, and steel pipes).
4 | Development of an ultrasonic system for detecting and profiling hydrate blockage in gas pipelines during operation. | Non-contact focused ultrasonic transducer, time-of-flight (TOF) analysis, 360° circumferential scanning, blockage contour reconstruction, and validation on a full-scale flow loop. | Real-time monitoring and early warning of hydrate blockage in operating natural gas pipelines.

## Slide 34
# | Focus | Approach | Main Application
5 | Review of ultrasonic guided-wave techniques for long-range pipeline inspection and structural health monitoring (SHM). | Ultrasonic guided waves, guided-wave transducers, signal processing, defect localization, and SHM technologies. | Non-destructive testing (NDT), pipeline integrity management, corrosion/crack detection, continuous pipeline monitoring.
6 | Detection and monitoring of solids deposition in slurry pipelines using electrical resistance tomography (ERT). | Electrical Resistance Tomography (ERT) with 16 circumferential electrodes to reconstruct cross-sectional conductivity maps and identify deposited solids in flowing slurry pipelines. | Online monitoring of slurry transport systems, sedimentation detection, and deposition onset in hydraulic conveying pipelines.

## Slide 35
Ref
El Mountassir, M., Yaacoubi, S., & Dahmene, F. (2020). Reducing false alarms in guided waves structural health monitoring of pipelines: Review synthesis and debate. International Journal of Pressure Vessels and Piping, 188, 104210.
Chen, P. (2025). Advancements and future outlook of safety monitoring, inspection and assessment technologies for oil and gas pipeline networks. Journal of Pipeline Science and Engineering, 5, 100267.
Lee, K. I. (2010). Ultrasonic technique for measuring the thickness of scale on the inner surfaces of pipes. Journal of the Korean Physical Society, 56(2), 558–561
Li, X., Liu, Y., Liu, Z., Chu, J., Song, Y., Yu, T., & Zhao, J. (2020). A hydrate blockage detection apparatus for gas pipeline using ultrasonic focused transducer and its application on a flow loop. Energy Science & Engineering, 8, 1770–1780
Zang, X., Xu, Z.-D., Lu, H., Zhu, C., & Zhang, Z. (2023). Ultrasonic guided wave techniques and applications in pipeline defect detection: A review. International Journal of Pressure Vessels and Piping, 206, 105033.
Fangary, Y. S., Williams, R. A., Neil, W. A., Bond, J., & Faulks, I. (1998). Application of electrical resistance tomography to detect deposition in hydraulic conveying systems. Powder Technology, 95, 61–66.

## Slide 36: Research Gaps

## Slide 37: Research Gaps
Fragmented prediction approaches Existing studies investigate thermodynamics, kinetics, transport, inhibitor modeling, AI, and monitoring independently. Few frameworks integrate these components into a unified operational scale prediction system.
Limited spatial understanding of scale deposition Most prediction models estimate scaling tendency or saturation index but do not reconstruct the spatial distribution of scale along pipelines, including deposition location, thickness, and growth evolution.
Limited utilization of multimodal sensing Existing monitoring techniques (ultrasonic, guided waves, tomography, pressure sensors, optical sensing, etc.) typically operate independently and are rarely fused with operational measurements and water chemistry to improve prediction accuracy.
Lack of spatio-temporal state estimation Current approaches generally predict whether scale forms, but they do not estimate the hidden spatio-temporal state of scale formation by combining sensor observations with mechanistic knowledge.

## Slide 38: Research Gaps
Static inhibitor management Current inhibitor dosage methodologies are primarily laboratory-based and static, with little capability to continuously adapt dosage using real-time measurements and predicted deposition behavior.
Weak integration with digital operations Few studies integrate prediction, sensor fusion, monitoring, inhibitor optimization, SCADA connectivity, and operational decision support into a single intelligent framework suitable for industrial deployment.

## Slide 39: Research Direction

## Slide 40: Research Direction
This research proposes an AI-based multimodal sensor fusion framework for intelligent scale management in surface flowlines. The framework integrates operational measurements, water chemistry, and multiple sensing technologies to reconstruct the spatio-temporal evolution of scale deposition and continuously estimate scale type, deposition location, thickness, growth, and scaling severity. These predictions are subsequently used to optimize inhibitor dosage and support real-time operational decision-making through an integrated digital platform.
Research Workflow
Historical & Laboratory Data
Multimodal Sensor Fusion
Spatio-Temporal Scale State Estimation
Physics-Informed AI Prediction
Adaptive Inhibitor Optimization
Digital Decision-Support Platform
Expected Outcome: A digital framework capable of continuously estimating where scale forms, how it evolves over time, and how inhibitor dosage should be adjusted to minimize scaling risk and operational cost.

## Slide 41: Objective 1
Develop an AI-Based Multimodal Sensor Fusion Framework for Spatio-Temporal Scale State Estimation
Goal Develop an AI framework that integrates operational data and multiple sensing technologies to continuously estimate the spatio-temporal evolution of scale deposition in surface flowlines.
Methodology
Develop a multimodal data acquisition framework integrating: Pressure sensors, Temperature sensors, Flow-rate measurements, Water chemistry measurements, Ultrasonic wave travel time, Guided-wave responses (or other compatible sensing technologies)
Perform data preprocessing, feature extraction, synchronization, and sensor fusion.
Develop AI models capable of learning relationships between multimodal measurements and scale behavior.
Estimate: Scale type, Deposition location, Deposit thickness, Growth rate, Scaling severity
Continuously update predictions using streaming operational data.
Validate using laboratory experiments, simulations, and historical field data.

## Slide 42: Objective 2
Develop an Adaptive Scale Inhibitor Optimization Framework
Goal
Utilize the estimated scale state to determine optimal inhibitor dosage under continuously changing operating conditions.
Methodology
Use outputs from the AI sensor-fusion framework.
Integrate: Predicted scale type, Deposition location, Deposit thickness, Growth rate, Water chemistry, Operating conditions
Optimize: Inhibitor concentration, and possibly Injection timing
Compare adaptive recommendations with conventional fixed-dosage strategies.
Evaluate improvements in inhibitor efficiency, chemical consumption, and scaling mitigation.

## Slide 43: Objective 3
Develop an Integrated Digital Decision-Support Platform
Goal: Develop a unified digital platform that combines prediction, monitoring, and optimization for intelligent scale management.
Methodology
Integrate: AI prediction module, Multimodal sensor fusion module, Scale state estimation, Inhibitor optimization
Visualize: Real-time scaling risk, Predicted scale type, Deposition location, Deposit thickness, Growth evolution, Inhibitor recommendations
Generate automated alerts and maintenance recommendations.
Design the framework for future deployment with industrial SCADA systems and digital oilfield infrastructure.