## Slide 1
AI-Driven Scale Formation Prediction
& Adaptive Inhibitor Optimization
Deep-dive proposal presentation for Scale Formation Prediction
Mujahed Al-Dhaifallah
Professor
KFUPM | Control & Instrumentation Engineering Department
Notes: Opening: Thank the Aramco team. State that the presentation is redesigned as a focused 10-minute deep-dive rather than a literature review.,Main message: an integrated physics-informed AI and sensor-fusion framework for predicting scale location, evolution, and inhibitor dosage.

## Slide 2
Industrial Need: prediction must be actionable
Scale formation is not only a chemistry problem; it is a flow-assurance decision problem.
Scale Formation Prediction
02
Scale types
CaCO₃ • BaSO₄ • SrSO₄ • Fe-based scales
Operational impact
• flow restriction
• pressure drop
• corrosion acceleration
• shutdown / intervention cost
Decision need
Where? What type? How severe? How much inhibitor?
Hidden deposition evolves along the line
The required output is a real-time scale state, not only a saturation-index number.
Aramco-facing outputs
Predict scale formation
before blockage or high-risk growth
Localize deposition
section-level risk map
Identify scale type
chemistry + sensor evidence
Optimize inhibitor
dose / timing / chemical use
Notes: Emphasize that Aramco’s problem requires an operational answer: location, severity, type, and dosage. Keep this slide under one minute.

## Slide 3
Current State: strong components, weak integration
The literature is mature in parts, but the industrial solution is still fragmented.
Scale Formation Prediction
03
Thermodynamics
SI / supersaturation
Fast screening, but weak spatial insight
Kinetics & MIC
induction time / tube blocking
Useful lab metrics, often static
Transport & deposition
CFD / mass transfer / adsorption
Captures flow effects, data intensive
AI & monitoring
ML / sensors / thickness estimation
Good prediction, limited physics & control
What is missing?
A closed-loop framework that fuses sensors + chemistry + operating data + mechanistic knowledge to estimate the hidden scale state and optimize inhibitor dosage continuously.
This is the core research gap and the proposed contribution.
Notes: Do not go through papers one by one. Say: we reviewed the work and grouped it into four streams. Each stream is valuable but none alone gives a field-ready closed-loop decision system.

## Slide 4
Proposed Solution: physics-informed AI sensor-fusion loop
The framework estimates the scale state and converts it into dosing decisions.
Scale Formation Prediction
04
Data layer
pressure, temperature, flow rate, water chemistry, sensors
Fusion layer
synchronization, feature extraction, uncertainty handling
Scale-state estimator
type, location, thickness, growth, severity
Optimization layer
inhibitor dose, timing, risk/cost trade-off
Physics-informed AI core
thermodynamics + kinetics + transport constraints
Digital decision platform
risk map • alerts • dashboards • recommendation history
Closed-loop learning
Novelty
• not only Scale / No Scale
• not only laboratory MIC
• spatial + temporal prediction
• adaptive operational decision
Notes: This is the central slide. Spend about two minutes. Explain the closed-loop logic: data is fused, hidden scale state is estimated, physics constrains AI, and inhibitor dosage is updated.

## Slide 5
Objective 1: Multimodal Sensor Fusion for Scale-State Estimation
Turn scattered measurements into a coherent real-time estimate of scale behavior.
Scale Formation Prediction
05
Pressure
ΔP trends
Temperature
thermal shifts
Flow rate
velocity / regime
Water chemistry
ions, TDS, pH
Ultrasonic / guided waves
thickness evidence
Historical data
maintenance / lab
Fusion Engine
• time alignment
• feature extraction
• noise filtering
• uncertainty weighting
• data-quality checks
Scale type
carbonate / sulfate / mixed
Location
where deposition starts
Thickness
current accumulation
Growth rate
future trajectory
Severity
risk index
Deliverable: a continuously updated “scale-state vector” for each monitored flowline section.
Notes: Keep it practical: data can come from available measurements first, and additional sensors can be added progressively. The deliverable is a state estimate, not a black-box classification only.

## Slide 6
Objective 2: Physics-Informed Spatio-Temporal Prediction
Use mechanistic knowledge to make AI predictions credible under changing operations.
Scale Formation Prediction
06
Physics constraints
• saturation index / supersaturation
• induction time
• nucleation & growth kinetics
• transport / mass transfer
• surface deposition / adsorption
Predicted scale evolution along the pipeline
t1
t2
t3
t4
flowline sections →
What the model predicts
• onset probability
• deposition thickness
• growth trajectory
• remaining safe operating window
• confidence bounds
Key benefit: extrapolation beyond the lab is constrained by chemistry and transport physics.
Notes: Explain why physics-informed AI matters to SMEs: pure ML may fail outside the training region; physics reduces implausible predictions and improves trust.

## Slide 7
Objective 3: Adaptive Inhibitor Optimization
Convert predicted risk into chemical-dose recommendations under operational constraints.
Scale Formation Prediction
07
MIC concept
Minimum inhibitor concentration that sufficiently delays or prevents scale under specified conditions.
Current practice
• fixed or lab-derived dose
• conservative margins
• limited adaptation
• field response after symptoms
Optimization engine
• risk target
• chemical cost
• dose limits
• injection timing
• operating window
minimize cost + risk
Adaptive recommendation
• optimal concentration
• injection timing
• expected risk reduction
• chemical saving estimate
• alarm if dose is insufficient
Output is explainable: tied to predicted scale type, location, growth, and confidence.
Notes: Define MIC quickly. Then emphasize the shift from static dosing to adaptive dose optimization that uses real-time scale-state estimates.

## Slide 8
Validation Strategy & Work Plan
A staged validation path reduces technical risk before industrial deployment.
Scale Formation Prediction
08
Phase 1
Data audit & baseline model
collect field variables, lab records, chemistry, existing scale reports
Phase 2
Laboratory / flow-loop validation
generate controlled scale-growth and inhibitor-response data
Phase 3
Physics-informed AI training
integrate thermodynamics, kinetics, transport, and sensor features
Phase 4
Digital prototype
dashboard, alerts, dosing recommendations, uncertainty
Phase 5
Field-readiness assessment
shadow-mode testing and deployment plan
Validation metrics
scale/no-scale accuracy • location error • thickness error • dosing reduction • false-alarm rate • decision latency
Notes: SMEs will ask about validation. This slide gives a realistic staged plan and metrics. It avoids overclaiming immediate field deployment.

## Slide 9
Expected Value to Aramco
A decision-support layer for proactive, optimized, and explainable scale management.
Scale Formation Prediction
09
Earlier warning
Detect rising scale risk before blockage.
Spatial localization
Prioritize the affected line section.
Chemical optimization
Reduce over-dosing while maintaining protection.
Operational continuity
Support intervention planning and shutdown avoidance.
Digital oilfield fit
Deployable as SCADA-connected advisory module.
Immediate next step
align on available data, target flowline, and validation scenario
Discussion
Notes: Close strongly. Emphasize value and request alignment on available data and target use case. Do not end with literature.

## Slide 10
Thank you